Control System Training
MODULE 5 – Sequential Boolean Logic

---
Copyright Notice
Copyright Notice
These training materials, including the samples, exercises, and solutions, are copyrighted materials. Any reproduction, or use of any kind without the specific written approval of the author is strictly prohibited.
Permission for extra-curricular use by First FRC teams for FRC related training is granted, provided the original copyright and acknowledgements are retained.
© Jim Simpson, 2018

---
Combinatorial Logic
Sequential Boolean Logic
Definitions:
  - Boolean – Only values are: ZERO / ONE or TRUE/FALSE
  - Sequential Logic -- Outcome depends on both current values of the inputs and previous values of the inputs and output.

---
Edge Triggered – ON
Edge Triggered – ON
Only true for a single scan.

---
Edge Triggered - OFF
Edge Triggered - OFF
Only true for a single scan

---
Edge Triggered - CHANGE
Edge Triggered - CHANGE
Only true for a single scan

---
One Shot
One Shot
Oneshot time is 0.200 seconds

---
On Delay
On Delay
- Delay is 0.200 Seconds
- If input goes false before delay expires, output is never true.

---
Off Delay
Off Delay
Off delay time is 0.080 seconds.

---
Set / Reset Flip Flop
Set / Reset Flip Flop
- Can think of this as “Boolean memory”. This is the building block of all computers.
- If both are true at the same time, one overrides the other. This is usually selectable.

---
Designing Sequential Logic 1/4
Designing Sequential Logic 1/4
Sample Problem – Cube Capture
  - Control system uses a 20 msec loop time
  - System is ready when “hand” is opened and “arm” is retracted
  - Users pushes button to initiate “cube capture”. Auto repeat of cube capture is not allowed.
  - Ensure user pushed button for 60 msec
  - Close “arm” extension solenoid. Wait 1 second for arm to extend.
  - Close “hand” solenoid. Wait 2.0 seconds for “hand” to settle.
  - Open “arm” extension solenoid. Wait 1.3 seconds for arm to retract.
  - Open “hand” solenoid to release potential cube into bin. Wait 1.5 seconds for cube to drop before allowing next “capture” action.
- Enhancement – Add a cancel button

---
Designing Sequential Logic 2/4
Designing Sequential Logic 2/4
Draw the Logic Diagram Graph

---
Designing Sequential Logic 3/4
Designing Sequential Logic 3/4
- Start with inputs
- Determine relationships
  - What inputs does an output relate to
- Draw Logic Diagram
- Add intermediate Logic to Graph
- Repeat last two steps if needed to refine logic

---
Designing Sequential Logic 4/4
Designing Sequential Logic 4/4
Final Logic Diagram

---
Designing Sequential Logic 4/4 - LabVIEW
Sample LabVIEW logic

---
Designing Sequential Logic 4/4 - LabVIEW
Alternate logic diagram – With Cancel

---
Designing Sequential Logic 4/4 - LabVIEW
Alternate sample LabVIEW logic – With Cancel

---
Exercise 5.2 – Shoot frisbee
Exercise 5.1 – Shoot Flying Disc
- Flying Disc shooter system has two outputs:
  - Shooting motor (on/off)
  - Solenoid to push flying disc into shooter wheel.
- Flying Disc shooter system has one sensor:
  - Limit switch indicating shooting system contains a flying disc.
- User pushes a button to shoot flying disc. Ensure user meant to push button. Button must be pressed for 0.060 seconds before initiating action. (Robot cycle time is 0.020 seconds).
- Only shoot a flying disc if system contains a disc. Also battery voltage must be > 11.5 volts. Only one disc can be shot at a time.
- Shooting motor takes 3 seconds to spin up to speed. Engage solenoid for 2 second to push flying disc into shooting wheel. Allow 2 more seconds for shooting to complete. After shooting is complete, stop motor. (For now, don’t allow continuous shooting.) It takes 5 seconds after shooting for the next flying disc to be in place ready to shoot.
- Allow user to press a Cancel button. The cancel button must be pressed for at least 0.060 seconds before becoming active. After the Cancel, force a 5 second reset before allowing a new shot.
- Design shooting logic. Also provide “ready to shoot” digital for dashboard display. Use ONLY the algorithms discussed in this module, and perhaps module 4.

---
Robot Programming 02
Complete Robot Programming Training 02

---
Exercise 5.2 – Shoot Flying Disc Robot Code
Implement the solution to 5.1 on a robot.
The limit switch inputs use:
Shooting system contains a flying disc – DIO 0
Battery voltage > 11.5 volts – DIO 1 (Alternatively find a library VI that provides battery voltage.
Shoot button – DIO 2
The outputs are:
Run motor – Relay 0 – (Forward only)
Shoot disc cylinder – dual solenoid –
PCM 0, channel 0 – shoot disc, channel 1 – normal position
Use the robot project “put-name-here”. The only VIs that need to be modified are in the “FlyingDiscShoot” sub-directory. They are:
FlyingDiscShoot_Open	- One time initialization goes here
FlyingDiscShoot_Execute	- Code to periodically execute goes here
10/30/2023
FRC Control System Training – © 2019 – J.A. Simpson