## Slide 1: FRC Robot Programming
MODULE 1 – Basics / Boolean In / Out

## Slide 2: Basic Robot Program
One time initialization actions
Continuous execution code cycles every 20 milliseconds.
  Faster or slower loops can be added if needed
Much more about this subject later

## Slide 3: WPILIB Robot Programming Palette
Function palette for all robot functions.

## Slide 4: Template Robot Project
Use existing template projects as the starting point for all robot code. (More about projects later.)
For the exercises there is already a project created ready for use.

## Slide 5: Compiling Robot Project
Robot Project must be compiled, “built”, before deploying to robot. Ensure code builds without errors!

## Slide 6: Deploying code to robot
Built robot project must be deployed to robot by selecting “run as startup”. Ensure this completes!
Then use Driver Station software to enable and test.

## Slide 7: Boolean Input – Limit Switch - Initialization
Initialization code
  Initialize hardware I/O
  Assign created data structure to “registry” for use by continuous execution routine.
  Note that this will be similar for ALL Input/Output (I/O) performed by the robot.
Limit Switch found under “sensors” sub palette

## Slide 8: Boolean Input – Limit Switch - Execution
Execution code
  Get “registry” entry for desired input
  Read current value from hardware.
  This code needs to be used every 20 milliseconds

## Slide 9: Network Table Variables
Network Table Variables
  Write values for use by:
    Display to drivers
    Trending operational performance and tuning
    Debugging
  Can both read and write values
Sample write

## Slide 10: Network Table Variables
Network tables uses “outline” style for naming variables.
  Variable names that start with “/” start at the top level.
  Variable names that start without a “/” start under “/SmartDashboard”
Names must be exact – Case is different, spaces are different
  This includes trailing spaces !!
Sample read

## Slide 11: Boolean Output – Digital Out - Initialization
Initialization code
  Initialize hardware I/O
  Assign created data structure to “registry” for use by continuous execution routine.
Digital Output found under I/O sub-palette

## Slide 12: Boolean Output – Digital Out - Execution
Execution code
  Get “registry” entry for desired input
  Read current value from hardware.
This code needs to be used every 20 milliseconds

## Slide 13: Exercise
Do Exercise 4.2 from Control Logic Training Module 4